## Slide 1: EN.601.414/614 Computer Networks Data Link Layer
Xin Jin
Spring 2018 (TTh 12:00-1:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
Data link layer

## Slide 3: Data link layer
Present everywhere
Transfers data between adjacent nodes or between nodes on the same local area network
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 4: Data link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection and correction

## Slide 5: Packets are now “frames”
Frames encapsulate network layer packets
Link layer protocols are implemented in h/w
Frame formats can change based on link layer protocol
sending
node
frame
receiving
node
data
frame
network
adaptor
network
adaptor
link layer protocol

## Slide 6: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 7: Multiple access algorithm
Context: a shared broadcast channel
  Must avoid having multiple nodes speaking at once
    Otherwise, collisions lead to garbled data
  Need distributed algorithm to determine which node can transmit
Three classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: scheme for deciding who transmits
  Random access: allow collisions, and then recover
    More in the Internet style!

## Slide 8: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 9: Ethernet
Invented as a broadcast technology
  Hosts share channel
  Each packet received by all attached hosts
  CSMA/CD for media access control
Modern Ethernets are “switched” (later)
  Point-to-point links between switches and between a host and switch
  No sharing  no CSMA/CD
    Uses “self learning” and “spanning tree” algorithms for routing

## Slide 10: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does not eliminate all collisions
  Why?

## Slide 11: CSMA collisions
Propagation delay: two nodes may not hear each other before sending
CSMA reduces but does not eliminate collisions
Collision: entire packet transmission time wasted
  Distance and propagation delay affect collision probability
Spatial layout of nodes

## Slide 12: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
  Later!
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 13: CSMA/CD (Collision Detection)
For this to work, need restrictions on minimum frame size and maximum distance
  Why?
Spatial layout of nodes

## Slide 14: Limits on CSMA/CD network length
Latency depends on physical length of link
  Time to propagate a frame from one end to other
Suppose A sends a frame at time t
  And B sees an idle line at a time just before t + d
  … so B happily starts transmitting a frame
B detects a collision, and sends jamming signal
  But A cannot see collision until t + 2d
latency d
A
B

## Slide 15: Limits on CSMA/CD network length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  AND keep an eye out for a possible collision
Imposes restrictions; e.g., for 10 Mbps Ethernet
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
latency d
A
B

## Slide 16: Three key ideas of random access
Carrier sense
  Listen before speaking and don’t interrupt
  Checking if someone else is already sending data
  … and waiting till the other node is done
Collision detection
  If someone else starts talking at the same time, stop
    Make sure everyone knows there was a collision!
  Realizing when two nodes are transmitting at once
  …by detecting that the data on the wire is garbled

## Slide 17: Three key ideas of random access
Randomness
  Don’t start talking again right away
  Waiting for a random time before trying again

## Slide 18: How long should you wait?
Should it be immediate?
Should it be a random number with a fixed distribution?

## Slide 19: Ethernet: CSMA/CD Protocol
Carrier sense: wait for link to be idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission & send jam signal
Random access: binary exponential back-off
  After collision, wait a random time before retrying
  After mth collision, choose K randomly from {0, …, 2m-1}
    Wait for K*512 bit times before trying again
    If transmission occurring when ready to send, wait until end of transmission (CSMA)

## Slide 20: Efficiency of CSMA/CD
Efficiency is defined as the long-run fraction of time during which frames are being transmitted without collision
dprop = max propagation time between two adapters
dtrans = time to transmit a max-sized frame
1
Efficiency ≈
1 + 5 dprop / dtrans

## Slide 21: Efficiency of CSMA/CD
dprop → 0
  Efficiency approaches 1
  Colliding nodes abort immediately
dtrans → ∞
  Efficiency approaches 1
  Each frames uses the channel for a long time
dtrans
Efficiency ≈
dtrans + 5 dprop

## Slide 22: Switched Ethernet

## Slide 23: Broadcast vs. switched Ethernet
Invented as a broadcast technology
  Hosts share channel
  Each packet received by all attached hosts
  CSMA/CD for media access control
Modern Ethernets are “switched”
  Point-to-point links between switches and between a host and switch
  No sharing  no CSMA/CD
    Uses “self learning” and “spanning tree” algorithms for routing

## Slide 24: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 25: The evolution of Ethernet
Changed almost everything except the frame format
  From the shared media coax cables to dedicated links
  From 3 Mbit/s to 100 Gbit/s
  From electrical signaling to optical
Lesson: the right interface can accommodate many changes
  Evolve the implementation while maintaining the interface (backward compatibility)

## Slide 26: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 27: Ethernet “Frames”
Encapsulates IP datagram
Preamble: 7 bytes for clock synchronization and 1 byte to indicate start of frame
Addresses: 6 bytes
Type: 2 bytes, higher-layer protocol (e.g., IP)
Data payload: max 1500 bytes, min 46 bytes
CRC: 4 bytes for error detection
type
Preamble
Dst Address
Source Address
Data
CRC

## Slide 28: Framing frames
Physical layer puts bits on a link
But, two hosts connected on the same physical medium need to be able to exchange frames
  Service provided by the link layer
  Implemented by the network adaptor
Framing problem: how does the link layer determine where each frame begins and ends?

## Slide 29: Simple approach: Count bytes
Sender includes number of bytes in header
  Receiver extracts this number of bytes of body
What if the Count field is corrupted?
  L2 will frame the wrong bytes  a framing error
  CRC tells you to discard this frame, but what about the next one?
53
Body
80
Body
53 bytes of data
80 bytes of data
61
Body
80
Body
61 bytes of data misdelivered
??? bytes of data misdelivered
???
Bogus count field

## Slide 30: Desynchronization
Once framing on a link is desynchronized, it can stay that way
Need a method to resynchronize

## Slide 31: Framing with sentinel bits
Delineate frame with special “sentinel” bit pattern
  e.g., 01111110  start, 01111111  end
What if sentinel occurs within frame?
Solution: bit stuffing
  Sender always inserts a 0 after five 1s in the frame contents
  Receiver always removes a 0 appearing after five 1s
01111110
01111111
Frame contents
Notes: 6 one’s  start
7 one’s  end

## Slide 32: When receiver sees five 1s…
If next bit 0, remove it; begin counting again
  Because this must be a stuffed bit; we can’t be at beginning/end of frame (those had six or seven 1s)
If next bit 1 (i.e., we’ve seen six 1s) then:
  If following bit is 0, this is start of frame
    Because the receiver has seen 01111110
  If following bit is 1, this is end of frame
    Because the receiver has seen 01111111
01111110
01111111
Frame content

## Slide 33: Example: sentinel bits
Original data, including start/end of frame:
  01111110011111101111101111100101111111
Sender rule: five 1s  insert a 0
  After bit stuffing at the sender:
  01111110011111010111110011111000101111111
Receiver rule: five 1s and next bit 0  remove 0
  01111110011111101111101111100101111111

## Slide 34: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 35: Medium Access Control (MAC) Address
MAC address
  Numerical address associated with a network adapter
  Flat name space of 48 bits (e.g., 00-15-C5-49-04-A9 in HEX)
  Unique, hard-coded in the adapter when it is built
Hierarchical Allocation
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
    First 24 bits (e.g., 00-15-C5-**-**-**)
  Adapter: assigned by the vendor from its block
    Last 24 bits

## Slide 36: MAC address vs. IP address
MAC Addresses
Hard-coded when adapter is built
Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
Like a social security number
Portable, and can stay the same as the host moves
Used to get packet between interfaces on same network
IP Addresses
Configured, or learned dynamically
Hierarchical name space of 32 bits (e.g., 12.178.66.9)
Like a postal mailing address
Not portable, and depends on where the host is attached
Used to get a packet to destination IP subnet

## Slide 37: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 38: Routing with switched Ethernet?
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 39: Why does Ethernet not use LS/DV?
Concerns over scalability
  Flat MAC addresses cannot be aggregated like IP addresses
Legacy

## Slide 40: “Routing” with broadcast Ethernet
Sender transmits frame onto broadcast link
Each receiver’s link layer passes the frame to the network layer:
  If destination address matches the receiver’s MAC address OR if the destination address is the broadcast MAC address (ff:ff:ff:ff:ff:ff)
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 41: “Routing” with broadcast Ethernet
Ethernet is “plug-n-play”
A new host plugs into the Ethernet and is good to go
  No configuration by users or network operators
  Broadcast as a means of bootstrapping comm.
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 42: Why does Ethernet not use LS/DV?
Concerns over scalability
  Flat MAC addresses cannot be aggregated like IP addresses
Legacy
  Backward compatibility with broadcast Ethernet
  Desire to maintain Ethernet’s plug-n-play behavior
  How broadcast Ethernet evolved

## Slide 43: Routing in extended LANs
Local-Area Network (LAN)
Bridges relay broadcasts from one LAN to the other

## Slide 44: The “broadcast storm” problem
Radia Perlman
Perlman’s idea: eliminate loops in the topology

## Slide 45: Easiest way to avoid loops
Use a topology where loops are impossible!
Take arbitrary topology and build a spanning tree
  Sub-graph that includes all vertices but contains no cycles
  Links not in the spanning tree are not used to forward frames

## Slide 46: Consider a graph

## Slide 47: A spanning tree

## Slide 48: Another spanning tree

## Slide 49: Yet another spanning tree

## Slide 50: Spanning tree protocol (Perlman’85)
Protocol by which bridges construct a spanning tree
Nice properties
  Zero configuration (by operators or users)
  Self healing
Still used today

## Slide 51: From extended LANs to switched Ethernet

## Slide 52: Switched Ethernet
Constraints (for backward compatibility)
  No changes to end-hosts
  Maintain plug-n-play aspect
Earlier Ethernet achieved plug-n-play by leveraging a broadcast medium
  Can we do the same in a switched topology?

## Slide 53: Summary
Data link layer transfers data between adjacent nodes or nodes connected to the same switch
Ethernet evolved from a broadcast medium to switched
Next week: Link layer wrap up + putting everything together

## Slide 54: Thanks! Q&A