## Slide 1: EN.601.414/614 Computer Networks Switched LAN
Xin Jin
Spring 2018 (TTh 12:00-1:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
Ethernet wrap-up
Putting everything together

## Slide 3: Recap: Switched Ethernet
Ethernet started as a broadcast medium
  Faced broadcast storm in larger setups due to flooding
Constraints of switched Ethernet (for backward compatibility)
  No changes to end-hosts
  Maintain plug-n-play aspect

## Slide 4: Ethernet topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 5: Flooding (still) leads to loops
Example: A wants to broadcast a message
  A sends packet to 1
  1 Floods to 2 and 4
  2 Floods to B and 3
  4 Floods to D and 3
  3 Floods packet from 2 to C and 4
  3 Floods packet from 4 to C and 2
  4 Floods packet from 3 to D and 1
  2 Floods packet from 3 to B and 1
  1 Floods packet from 2 to A and 4
  1 Floods packet from 4 to B and 2
  ….
Broadcast storm still happens in a switched network if it contains a cycle of switches
1
2
4
3
B
A
C
D

## Slide 6: Spanning tree approach
Take arbitrary topology
Pick subset of links that form a spanning tree

## Slide 7: Algorithm has two aspects
Pick a root
  Destination to which shortest paths go
  Pick the one with the smallest identifier (MAC addr.)
Compute shortest paths to the root
  No shortest path can have a cycle
  Only keep the links on shortest-paths
  Break ties in some way (so we only keep one shortest path from each node)
Ethernet’s spanning tree construction does both with a single algorithm

## Slide 8: Breaking ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID
  One could use any tiebreaking system, but this is an easy one to remember and implement

## Slide 9: Constructing a spanning tree
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switches elect the node with smallest identifier (MAC address) as root
Each switch determines if a link is on its shortest path to the root; excludes it from the tree if not

## Slide 10: Steps in the spanning tree algorithm
Initially, each switch proposes itself as the root
  Switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 11
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)

## Slide 12: Robust spanning tree algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
Root switch sends periodic root announcement messages
  Other switches continue forwarding messages
Detecting failures through timeout
  If no word from root, time out and claim to be the root!

## Slide 13: Ethernet topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 14: Flooding on a spanning tree
Switches flood using the following rule:
  (Ignore all ports not on spanning tree!)
  Originating switch sends packet out all ports
  When a packet arrives on one incoming port, send it out all ports other than the incoming port

## Slide 15: Flooding on spanning tree

## Slide 16: Flooding on spanning tree

## Slide 17: But isn’t flooding wasteful?
Yes, but we can use it to bootstrap more efficient forwarding
Idea: watch the packets going by, and learn from them
  If node A sees a packet from node B come in on a particular port, it knows what port to use to reach B!
  Works because there is only one path to B

## Slide 18: Nodes can “learn” routes
Switch learns how to reach nodes by remembering where flooding packets came from
  If flood packet from Node A entered switch on port 4, then switch uses port 4 to send to Node A

## Slide 19: General approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded

## Slide 20: Learning from flood packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 21: Node B responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 22: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 23: Self learning: Handling misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response may teach switch about that destination
A
B
C
D

## Slide 24: Summary of learning approach
Avoids loop by restricting to spanning tree
  This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No route “computation”
Forwarding entries a consequence of traffic pattern

## Slide 25: Contrast
IP
Packets forwarded on all available links
Addresses can be aggregated
Routing protocol computes loop-free paths
Forwarding table computed by routing protocol
Ethernet
Packets forwarded on subset of links (spanning tree)
Flat addresses
“Routing” protocol computes loop-free topology
Forwarding table derived from data packets(+ spanning tree for floods)

## Slide 26: Strengths of Ethernet’s approach
Plug-n-Play: zero-configuration / self-*
Simple
Cheap?

## Slide 27: Weaknesses of Ethernet’s approach
Much of the network bandwidth goes unused
  Forwarding is only over the spanning tree
Delay in reestablishing spanning tree
  Network is “down” until spanning tree rebuilt
  Rebuilt spanning tree may be quite different
Slow to react to host movement
  Entries must time out
Poor predictability
  Location of root and traffic pattern determines forwarding efficiency

## Slide 28: Link layer topics
Frames and framing
Addressing
Routing
Forwarding
Discovery and bootstrapping

## Slide 29: Discovery
A host is “born” knowing only its MAC address
Must discover lots of information before it can communicate with a remote host B
  What is my IP address?
  What is B’s IP address? (remote)
  What is B’s MAC address? (if B is local)
  What is my first-hop router’s address? (if B is not local)
  …

## Slide 30: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability
Hosts
Router

## Slide 31: ARP and DHCP
Link layer discovery protocols
Serve two functions
  Discovery of local end-hosts
    For communication between hosts on the same LAN
  Bootstrap communication with remote hosts
    What’s my IP address?
    Who/where is my local DNS server?
    Who/where is my first hop router?

## Slide 32: DHCP
Dynamic Host Configuration Protocol
  Defined in RFC 2131
A host uses DHCP to discover
  Its own IP address
  Its netmask
  IP address(es) for its local DNS name server(s)
  IP address(es) for its first-hop “default” router(s)

## Slide 33: DHCP: Operation
One or more local DHCP servers maintain required information
  IP address pool, netmask, DNS servers, etc.
  Application that listens on UDP port 67

## Slide 34: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
  L2 broadcast, to MAC address FF:FF:FF:FF:FF:FF

## Slide 35: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
  Proposed IP address for client, lease time
  Other parameters

## Slide 36: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
  Specifies which offer it wants
  Echoes accepted parameters
  Other DHCP servers learn they were not chosen

## Slide 37: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 38: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK
DHCP “relay agents” used when the DHCP server is not on the same broadcast domain

## Slide 39: DHCP uses “soft state”
Soft state: if not refreshed, state is forgotten
  Hard state: allocation/revocation is deliberate
Implementation:
  Address allocations have a lease period
  Server sets a timer for each allocation
  Client must request a refresh before lease expires
  Server resets timer when a refresh arrives and ACKs
    OR reclaims allocated address when timer expires
Simple, yet robust under failure

## Slide 40: Soft state under failure
What happens when host XYZ fails?
  Refreshes from XYZ stop
  Server reclaims a.b.c.d after O(lease period)
Router
XYZ
DHCP Server
a.b.c.d is mine from (now’, now’+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 41: Soft state under failure
What happens when server fails?
  ACKs from server stop
  XYZ releases address after O(lease period); send new request
  A new DHCP server can come up from a `cold start’ and we are back on track in ~lease time
Router
XYZ
DHCP Server
a.b.c.d is mine from (now’, now’+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 42: Soft state under failure
What happens if the network fails?
  Refreshes and ACKs don’t get through
  XYZ release address; DHCP server reclaims it
Router
XYZ
DHCP Server
a.b.c.d is mine from (now’, now’+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 43: Are we there yet?
DHCP Server
DNS Server
Router
Host
Host
Host
Host
What I learnt from DHCP
my IP: 1.2.3.48
netmask: 1.2.3.0/24 (255.255.255.0)
Local DNS: 1.2.3.156
router: 1.2.3.19

## Slide 44: Sending packets over link Layer
Link layer only understands MAC addresses
  Translate the destination IP address to MAC address
  Encapsulate the IP packet in a link-level (Ethernet) frame
Router
Host
Host
Host
Host
DNS
1.2.3.48
1.2.3.156
58-23-D7-FA-20-B0
90-E2-A1-09-66-1B
1.2.3.53
1.2.3.156
IP packet
DHCP Server

## Slide 45: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 46: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 47: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 48: ID resolution in the networking stack
Layer | Examples | Structure | Configuration | Resolution Service
App. Layer | cse.umich.edu | Organizational hierarchy | ~ manual | 
Network Layer | 123.45.6.78 | topological hierarchy | DHCP | 
Link layer | 45-CC-4E-12-F0-97 | vendor (flat) | hard-coded | 
DNS
ARP

## Slide 49: Discovery mechanisms
We have seen two approaches
  Broadcast (ARP, DHCP)
    Flooding does not scale
    No centralized point of failure
    Zero configuration
  Directory service (DNS)
    No flooding / scalable
    Root of the directory is vulnerable (caching is key)
    Needs configuration to bootstrap (local, root servers, etc.)

## Slide 50: Summary
Spanning tree enables Ethernet to efficiently flood a network to learn routes while forwarding packets
DHCP and ARP form the discovery backplane of networking and make everything work together
Next lecture: SDN

## Slide 51: Thanks! Q&A