## Slide 1: EN.601.414/614 Computer Networks Midterm Review
Xin Jin
Spring 2018 (TTh 12:00-1:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Midterm Exam
Time: 12-1:15pm March 15 (this Thursday)
Location: Shaffer 301
Form: Closed-book
  Can bring one A4/letter paper with notes on both sides
  Can bring a calculator
  Anything else is prohibited

## Slide 3: This review
Walk through what you’re expected to know at this point: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Summarize, not explain
  Stop me when you want to discuss something further!

## Slide 4: Topics
Basics (lectures 2–3)
Application layer (lectures 4, 5, 7)
  HTTP, DNS, and CDN
  Video Streaming
Wireless networks (lecture 6)
Transport layer (lectures 8–11)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lectures 12)
  Data plane

## Slide 5: Basic concepts
You should know:
  Packet vs. circuit switching
  Statistical multiplexing
  Link characteristics
  Packet delays

## Slide 6: How are network resources shared?
Two approaches
  Reservations  circuit switching
  On-demand  packet switching

## Slide 7: Two approaches to sharing
Packet switching
  Network resources consumed on demand per-packet
  Admission control: per packet
Circuit switching
  Network resources reserved a priori at “connection” initiation
  Admission control: per connection

## Slide 8: Circuit switching
src sends reservation request to dst
Switches create circuit after admission control
src sends data
src sends teardown request
dst
src
10 Mbps?
10 Mbps?
✔️
✔️

## Slide 9: Packet switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance

## Slide 10: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Good for bursty traffic (average << peak demand)
  Packet switching exploits statistical multiplexing better than circuit switching

## Slide 11: Performance metrics
Delay
Loss
Throughput

## Slide 12: A network link
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time
BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 13: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 14: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 15: OSI layers
OSI stands for Open Systems Interconnection model
  Developed by the ISO
Session and presentation layers are often implemented as part of the application layer
Application
Presentation
Session
L7
L6
L5
Transport
Network
Data link
Physical
L4
L3
L2
L1

## Slide 16: Layers in practice
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 17: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 18: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 19: Topics
Basics (lectures 2–3)
Application layer (lectures 4, 5, 7)
  HTTP, DNS, and CDN
  Video Streaming
Wireless networks (lecture 6)
Transport layer (lectures 8–11)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lectures 12)
  Data plane

## Slide 20: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 21: Steps in HTTP request/response
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
.
.
.
Establish
connection
Request
response
Client
request
Close connection

## Slide 22: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 23: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 24: Content Distribution Networks (CDN)
Caching and replication as a service
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 25: Hierarchies in the DNS
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 26: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
princeton.edu servers

## Slide 27: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
princeton.edu servers
www.princeton.edu?
(mydns.jhu.edu)

## Slide 28: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
www.princeton.edu?
princeton.edu servers
(mydns.jhu.edu)

## Slide 29: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
(mydns.jhu.edu)
www.princeton.edu?
princeton.edu servers

## Slide 30: Name resolution: Recursive
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
(mydns.jhu.edu)
www.princeton.edu?
princeton.edu servers

## Slide 31: Name resolution: Iterative
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
www.princeton.edu?
princeton.edu servers

## Slide 32: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.cnn.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 33: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while. Why?
  To minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 34: Datacenter networks (Cont.)
Rack
Aggregation
Core

## Slide 35: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 36: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 37: Topics
Basics (lectures 2–3)
Application layer (lectures 4, 5, 7)
  HTTP, DNS, and CDN
  Video Streaming
Wireless networks (lecture 6)
Transport layer (lectures 8–11)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lectures 12)
  Data plane

## Slide 38: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving at destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 39: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues
  Hidden terminal problem

## Slide 40: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 41: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Notes: 41

## Slide 42: Topics
Basics (lectures 2–3)
Application layer (lectures 4, 5, 7)
  HTTP, DNS, and CDN
  Video Streaming
Wireless networks (lecture 6)
Transport layer (lectures 8–11)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lectures 12)
  Data plane

## Slide 43: Role of the transport layer
(1) Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports
(2) Provide common end-to-end services for app layer
  Reliable, in-order data delivery
  Well-paced data delivery

## Slide 44: UDP vs. TCP
 | UDP | TCP
Data abstraction | Packets (datagrams) | Stream of bytes of arbitrary length
Service | Best-effort (same as IP) | Reliability In-order delivery Congestion control Flow control
  Both UDP and TCP perform mux/demux via ports

## Slide 45: Reliable transport: General concepts
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments (feedback from receiver)
  Cumulative: “received everything up to X”
  Selective: “received X”
Sequence no (detect duplicates, accounting)
Sliding windows (for efficiency)
You should know:
what these concepts are
why they exist
how TCP uses them

## Slide 46: Designing a reliable transport protocol
Stop and wait is correct but inefficient
  Works packet by packet (of size DATA)
  Throughput is (DATA/ RTT)
Sliding window: use pipelining to increase throughput
  n packets at a time results in higher throughput
  MIN(n*DATA/RTT, Link Bandwidth)

## Slide 47: The TCP abstraction
TCP delivers a reliable, in-order, byte stream
Reliable: TCP resends lost packets (recursively)
  Until it gives up and shuts down connection
In-order: TCP only hands consecutive chunks of data to application
Byte stream: TCP assumes there is an incoming stream of data, and attempts to deliver it to app

## Slide 48: Things to know about TCP
How TCP achieves reliability
RTT estimation
Connection establishment/teardown
Flow Control
Congestion Control
For each, know how the functionality is implemented and why it is needed

## Slide 49: Reliability
Having TCP take care of it simplifies application development
How
  Checksums and timers (for error and loss detection)
  Fast retransmit (to detect faster-than-timeout loss)
  Cumulative ACKs (receiver feedback: what’s lost?)
  Sliding windows (for efficiency)
  Buffers at sender (hold packets until ACKs arrive)
  Buffers at receiver (to reorder packets before delivery to application)

## Slide 50: RTT estimation
TCP uses timeouts to retransmit packets
  But RTT may vary (significantly!) for different reasons and on different timescales
    due to temporary congestion
    due to long-lived congestion
    due to a change in routing paths
An incorrect RTT estimate might introduce spurious retransmissions or overly long delays
Proposed solutions use EWMA, incorporate deviations

## Slide 51: Establishing a TCP connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
Three-way handshake to terminate (normal operation)
SYN
SYN ACK
ACK
A
B
Data
Data

## Slide 52: Flow control
Why?
  TCP at the receiver must buffer a packet until all packets before it (in byte-order) have arrived and the receiving application has consumed available bytes
  Hence, receiver advances its window when the receiving application consumes data
  Sender advances its window when new data ACK’d
  Risk of sender over-runing the receiver’s buffers
How?
  “Advertised Window” field in TCP header

## Slide 53: Congestion control
Why?
  Because the network itself can be the bottleneck
  Should make efficient use of available network capacity
    While sharing available capacity fairly with other flows
    And adapting to changes in available capacity
How?
  Dynamically adapts the size of the sending window

## Slide 54: Put together
Flow Control
  Restrict window to RWND to make sure that the receiver isn’t overwhelmed
Congestion Control
  Restrict window to CWND to make sure that the network isn’t overwhelmed
Together
  Restrict window to min{RWND, CWND} to make sure that neither the receiver nor the network are overwhelmed

## Slide 55: CC implementation
States at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  dupACKcount and timer
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 56: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence, after one RTT with no drops: CWND = 2xCWND

## Slide 57: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence, after one RTT with no drops: CWND = CWND + 1
Congestion avoidance phase

## Slide 58: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 59: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 60: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 61: TCP flavors
TCP-Tahoe
  CWND =1 on 3 dupACKs
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on 3 dupACKs
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  Incorporates selective acknowledgements
Our default assumption

## Slide 62: A simple model for TCP throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 63: A simple model for TCP throughput
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 64: Implications on High-speed TCP
Assume RTT = 100ms, MSS=1500bytes, BW=100Gbps
What value of p is required to reach 100Gbps throughput?
  ~ 2 x 10-12
How long between drops?
  ~ 16.6 hours
How much data has been sent in this time?
  ~ 6 petabits

## Slide 65: Topics
Basics (lectures 2–3)
Application layer (lectures 4, 5, 7)
  HTTP, DNS, and CDN
  Video Streaming
Wireless networks (lecture 6)
Transport layer (lectures 8–11)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control: general concepts only
Network layer (lectures 12)
  Data plane

## Slide 66: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 67: Designing the IP header
Think of the IP header as an interface
  Between the source and destination end-systems
  Between the source and network (routers)
Designing an interface
  What task(s) are we trying to accomplish?
  What information is needed to do it?
Header reflects information needed for basic tasks

## Slide 68: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  Loops: TTL (8 bits)
  Corruption: checksum (16 bits)
  Packet too large: fragmentation fields (32 bits)

## Slide 69: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Identification
13-bit
Fragment Offset
3-bit
Flags
16-bit
Header Checksum
8-bit
Protocol
8-bit
TTL
32-bit
Source IP Address
32-bit
Destination IP Address
Options (if any)

## Slide 70: IPv4 and IPv6 header comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
128-bit Source Address |  |  |  | 
128-bit Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 71: Philosophy of changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation and checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 72: Thanks! Q&A