## Slide 1: EN.601.414/614 Computer Networks Protocol Layering
Xin Jin
Fall 2020 (TuTh 1:30-2:45pm on Zoom)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
How is communication organized?

## Slide 3: Inspiration…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B

## Slide 4: Inspiration…
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 5: The path of the letter
CEO
Aide
FedEx
CEO
Aide
FedEx
FedEx Envelope
Letter
Envelope

## Slide 6: The path of the letter
CEO
Aide
FedEx
CEO
Aide
FedEx
“Peers” in same layer understand each other
No one else needs to
Lowest level has most packaging
Letter
Envelope
Semantic Content
Identity
FedEx Envelope
Location

## Slide 7: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 8: Back to the Internet: Decomposition
Applications
Physical transfer of bits
Best-effort local packet delivery
Best-effort global packet delivery
Reliable or unreliable transport
in built on
in built on
in built on
in built on

## Slide 9: Communication organization
Application
Applications
Physical transfer of bits
Best-effort local packet delivery
Best-effort global packet delivery
Reliable or unreliable transport
in built on
in built on
in built on
in built on
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 10: OSI layers
OSI stands for Open Systems Interconnection model
  Developed by the ISO
Session and presentation layers are often implemented as part of the application layer
Application
Presentation
Session
L7
L6
L5
Transport
Network
Data link
Physical
L4
L3
L2
L1

## Slide 11: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 12: Layers and protocols
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
Communication between peer layers on different systems is defined by protocols
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 13: What is a Protocol?
Friendly greeting
Time?
12:10 PM
Thanks! Let’s start
Friendly greeting

## Slide 14: What is a Protocol?
Data
An agreement between parties (in the same layer) on how to communicate
Defines the syntax of communication
  Header  instructions on how to process payload
  Each protocol defines the format of its headers
    e.g., “the first 32 bits carry the destination address”
Data
Payload
Header

## Slide 15: What is a Protocol?
An agreement between parties (in the same layer) on how to communicate
Defines the syntax of communication
And semantics
  “First a hello, then a request…”
  We will study many protocols later in the semester
Protocols exist at many levels, hardware, and software
  Defined by standards bodies like IETF, IEEE, ITU

## Slide 16: Protocols at different layers
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS
Notes: SMTP (Simple Mail Transfer Protocol); FDDI (Fiber Distributed Data Interface); PPP (Point-to-Point Protocol); PSTN (Public Switched Telephone Network)

## Slide 17: A Plethora of Protocol Acronyms
BGP
ARP
HTTP
DNS
PPP
OSPF
DHCP
TCP
UDP
SMTP
FTP
SSH
MAC
IP
RIP
NAT
CIDR
VLAN
VTP
NNTP
POP
IMAP
RED
ECN
SACK
SNMP
TFTP
TLS
WAP
SIP
IPX
STUN
RTP
RTSP
RTCP
PIM
IGMP
ICMP
MPLS
LDP
HIP
LISP
LLDP
BFD
Notes: Most have three or four letters, except IP has just two. But IP is special, as it is the center of the known universe.
Red: network layer
Green: transport layer
Purple: application layer
Blue: routing
Yellow: enterprise/edge networks
Black: other stuff
WAP: Wireless Application Protocol
SIP: Session Initiation Protocol
PPP: Point-to-Point Protocol
IPX: Internetwork Packet Exchange
HIP: Host Identity Protocol (HIP)
IGMP: Internet Group Management Protocol, multicast
ICMP: Internet Control Message Protocol, e.g., ping, traceroute
RTP: Real-time Transport Protocol
PIM: Protocol-Independent Multicast
RED: Random early detection
RTCP: RTP Control Protocol (RTCP)
RIP: Routing Information Protocol
SMTP: Simple Mail Transfer Protocol
RTSP: Real Time Streaming Protocol
BFD: Bidirectional Forwarding Detection
CIDR: Classless Inter-Domain Routing
NNTP: Network News Transfer Protocol
STUN: Session Traversal Utilities for NAT
VTP: VLAN Trunk Protocol
POP: Post Office Protocol
LISP: Locator/ID Separation Protocol
TFTP: Trivial File Transfer Protocol
LDP: Label Distribution Protocol

## Slide 18: ONE network layer protocol
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 19: What do students say about this course?
“In the computer networks class, I fell asleep at the start of the semester when the IP header was on the screen, and woke up at the end of the semester with the TCP header on the screen.”
“Network class final: ARP, DHCP, ICMP, IGMP, IP, TCP, UDP.”
Notes: ICMP is short for Internet Control Message Protocol. It is an extension to the Internet Protocol (IP) defined by RFC 792. ICMP supports packets containing error, control, and informational messages. It is an error reporting protocol and is used by routers, hosts and network devices to generate error messages when there are problems delivering IP packets.
The Internet Group Management Protocol (IGMP) is a communications protocol used by hosts and adjacent routers on IPv4 networks to establish multicast group memberships.

## Slide 20: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 21: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 22: What get’s implemented where?
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1

## Slide 23: What gets implemented at the end systems?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 24: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  data link layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
The network does not support reliable delivery
  Transport layer (and above) at end systems supports

## Slide 25: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Data link
Physical
Transport
Network
Data link
Physical
Network
Data link
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 26: A closer look: End system
Application
  Web server, browser, mail, game
Transport and network layer
  typically part of the operating system
Data link and physical layer
  hardware/firmware/drivers

## Slide 27: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  data link layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
Switches implement only physical and datalink layers (L1, L2)
Routers implement the network layer too (L1, L2, L3)

## Slide 28: A closer look at the network
switch
link
Internet Service Provider
switch
link

## Slide 29: A closer look at the network
switch
link
Internet Service Provider
routers
switch
link

## Slide 30: Switches vs. Routers
Switches do what routers do but don’t participate in global delivery, just local delivery
  Switches only need to support L1, L2
  Routers support L1-L3
Won’t focus on the router/switch distinction
  Almost all boxes support network layer these days

## Slide 31: Logical communication
A layer interact with its peers corresponding layer
Transport
Network
Data link
Physical
Transport
Network
Data link
Physical
Network
Data link
Physical
Application
Application
End system
End system
Switch

## Slide 32: Physical communication
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Data link
Physical
Transport
Network
Data link
Physical
Network
Data link
Physical
Application
Application
End system
End system
Switch

## Slide 33: A protocol-centric diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Notes: SONET (Synchronous Optical NETworking)

## Slide 34: Pros and cons of layering
Why layers?
Reduce complexity
Improve flexibility
Why not?
Higher overheads
Cross-layer information often useful

## Slide 35: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 36: Implications of hourglass
Single network-layer protocol (IP)
Allows arbitrary networks to interoperate
  Any network that supports IP can exchange packets
Decouples applications from low-level networking technologies
  Applications function on all networks
Supports simultaneous innovations above and below IP
But changing IP itself is hard (e.g., IPv4  IPv6)

## Slide 37: Placing network functionality
End-to-end arguments by Saltzer, Reed, and Clark
  Dumb network and smart end systems
  Functions that can be completely and correctly implemented only with the knowledge of application end host, should not be pushed into the network
  Sometimes necessary to break this for performance and policy optimizations
  Fate sharing: fail together or don’t fail at all
Notes: The fate-sharing model suggests that it is acceptable to lose the state information associated with an entity if, at the same time, the entity itself is lost. Specifically, information about transport level synchronization is stored in the host which is attached to the net and using its communication service.

## Slide 38: Assignment 1
Socket Programming
  Socket: communication endpoint at the end hosts
  Provide an application interface to exchange data between processes.
Server side
  socket()  bind()  listen()  accept()  recv()  close()
Client side
  socket()  connect()  send()  close()

## Slide 39: Group Discussion
Topic: protocol layering
  What are the five layers?
  Pick a functionality. Should the functionality be implemented in the end systems or the network? Why?
    Example functionalities: compute forwarding path, handle packet loss, handle packet retransmission, packet packet corruption, handle packet reordering, etc.
Discuss in groups, and each group chooses a leader to summarize the discussion
  In your group discussion, please do not dominate the discussion, and give everyone a chance to speak

## Slide 40: Summary
Layering is a good way to organize networks
Unified Internet layer decouples applications from networks
E2E argument encourages us to keep IP simple
Assignment 1 is out

## Slide 41: Thanks! Q&A