## Slide 1: EN.601.414/614 Computer Networks Security
Xin Jin
Spring 2018 (TTh 12:00-1:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
Common security issues and challenges in the network stack

## Slide 3: Layers in the network stack
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 4: Layer 7: Too many to cover
Layer 7 applications present a wide range of diverse threats
  Server-side vulnerabilities (e.g., buffer overflow, SQL injection, XSS), spam, phishing, account theft, …
  Leading to many cybercrimes
Not our focus

## Slide 5: General goals for communication security: CIA
Confidentiality
  No one read our communication
  Cryptography
Message Integrity
  No one can modify our communication w/o detection
  Verification
Availability and Authentication
  Only we can access our data and communicate on our behalf
  Redundancy, DoS/DDoS prevention

## Slide 6: A quick look at TCP

## Slide 7: Layer 4: Manipulation of TCP
Source and destination port/IP define a connection
Sequence number of a packet define its place in the stream
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 8: TCP’s 3-Way handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
connect()
listen()
ACK, SeqNum = x + 1, Ack = y + 1, Data = “GET”
ACK, SeqNum = y + 1, Ack = x + 10, Data = “200”

## Slide 9: TCP abrupt termination
A sends a RESET (RST) to B
  E.g., because application process on A crashed
That’s it
  B does not ack the RST
  Thus, RST is not delivered reliably, and any data in flight is lost
An attacker who knows ports and sequence numbers can disrupt any TCP connection
SYN
SYN ACK
ACK
Data
RST
ACK
time
A
B

## Slide 10: TCP RST injection
Client (initiator)
Server
connect()
listen()
ACK, SeqNum = x + 1, Ack = y + 1, Data = “GET”
ACK, SeqNum = y + 1, Ack = x + 10, Data = “200”
RST, SeqNum = y + 1, Ack = x + 10
Attacker
Client removes connection and will ignore ALL future comm.

## Slide 11: Connection hijacking
Taking over an already-established connection instead of RST injection
  Even worse!

## Slide 12: TCP data injection
Client (initiator)
Server
connect()
listen()
ACK, SeqNum = x + 1, Ack = y + 1, Data = “GET”
ACK, SeqNum = y + 1, Ack = x + 10, Data = “200”
ACK, SeqNum = y + 1, Ack = x + 10, Data = “200”
Attacker
Client processes the WRONG data
ACK, SeqNum = y + 1, Ack = x + 10, Data = “200”
Client ignores ACK-ed data

## Slide 13: Connection hijacking
Taking over an already-established connection instead of RST injection
  Even worse!
Root cause
  Attacker can see packet contents and thus knows port/IP and SeqNum

## Slide 14: Secure Sockets Layer (SSL)
Transport layer security for TCP-based apps
Used between Web browsers and servers (HTTPS)
Security services:
    Server authentication (is it really your bank’s server?)
    Data encryption (transaction not altered)
    Client authentication (optional)
SSLv3 was the ancestor of IETF’s Transport Layer Security (TLS)

## Slide 15: SSL/TLS and TCP/IP
SSL provides application programming interface (API) to applications
C and Java SSL libraries/classes readily available
Application
TCP
IP
Normal application
Application
SSL/TLS
TCP
IP
Application with SSL

## Slide 16: TCP security issues
An attacker who can observe packets, can
  Forcefully RST connections
  Inject forged data
  A major challenge today
SSL/TLS provide
  Confidentiality
  Data integrity
  Authentication
SSL/TLS can handle data injection but not RST injection

## Slide 17: A quick security analysis of the IP header

## Slide 18: Focus on sender attacks
Vulnerabilities sender can exploit
Ignore (for now) attacks by others
  Traffic analysis
  Snooping payload
  Denial of service

## Slide 19: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Identification
13-bit
Fragment Offset
3-bit
Flags
16-bit
Header Checksum
8-bit
Protocol
8-bit
TTL
32-bit
Source IP Address
32-bit
Destination IP Address
Options (if any)
Payload

## Slide 20: IP address integrity
Source address should be the sending host
  But, you could send packets with any source you want
Notes: No notion of identity that has any cryptographic binding to address (or any kind of binding that is visible to network).

## Slide 21: Implications of IP address integrity
Why would someone use a bogus source address?
Launch a denial-of-service attack
  Send excessive packets to the destination to overload the node, or the links leading to the node
  But: victim can identify/filter you by the source address
Evade detection by “spoofing”
  Put someone else’s source address in the packets
    Or: use many different ones so can’t be filtered

## Slide 22: More security implications
IP options
  Misuse: e.g., Source Route lets sender control path taken through network - say, sidestep security monitoring
  IP options often processed in router’s slow path  attacker can try to overload routers
Firewalls often configured to drop packets with options

## Slide 23: Security implications of ToS
Attacker sets ToS priority for their traffic
  If regular traffic does not set ToS, then network prefers the attack traffic, greatly increasing damage
Today, network ToS generally does not work
  ToS now redefined for differentiated service
  Mostly set/used by network operators, not end-systems

## Slide 24: Security implications of fragmentation
Allows evasion of network monitoring/enforcement
E.g., split an attack across multiple fragments
  Packet inspection won’t match a “signature”
Monitor must remember previous fragments
  But that costs state, which is another vector of attack
Nasty-at
Offset=0
tack-bytes
Offset=8

## Slide 25: More fragmentation attacks
What happens if attacker doesn’t send all of the fragments in a packet?
Receiver (or firewall) winds up holding the ones they receive for a long time
  State-holding attack

## Slide 26: Security implications of TTL
Allows discovery of topology (a la traceroute)
Can provide a hint that a packet is spoofed
  It arrives at a router w/ a TTL different than packets from that address usually have
    Because path from attacker to router has different # hops
  Brittle in the presence of routing changes
Initial value is somewhat distinctive to sender’s operating system. This plus other such initializations allow OS fingerprinting …
  Which allow attacker to infer its likely vulnerabilities

## Slide 27: Other security implications
No apparent problems with the protocol field
  It’s just a de-muxing handle
  If set incorrectly, next layer will find packet ill-formed
Bad IP checksum field will cause packet to be discarded by the network
  Not an effective attack

## Slide 28: Preventing (some) network layer threats

## Slide 29: Security at the network layer
There are security concerns that apply to multiple applications and cut across protocol layers
Benefits of network-layer security
  Below transport layer: transparent to applications
  Can be transparent to end users
  Helps secure routing architecture

## Slide 30: IPsec: Network layer security
Provides
  Network-layer authentication: destination host can authenticate source IP address
  Network-layer confidentiality and integrity:
    Sending host encrypts the data in IP datagram
Two principle protocols:
  Authentication header (AH) protocol
  Encapsulation security payload (ESP) protocol
  Mandatory in IPv6, optional in IPv4

## Slide 31: IPsec transport mode
IPsec datagram emitted and received by end-system
Protects upper level protocols
The routers/switches can also be IPsec-aware
IPsec
IPsec

## Slide 32: Virtual Private Network (VPN)
VPN makes separated IP sites look like one private IP network
    Private addresses and domain names (useful for authorization)
Security via IPsec tunnels
Simplified network operation: ISP can do the routing for you
Building a real private network is expensive (cheaper to use shared resources rather than to have dedicated resources)

## Slide 33: End-to-end VPNs
Solves the problem of connecting remote hosts to a firewalled network
  Commonly used for roaming
  Benefits in the form of security and private addresses only
Site (private network)
Internet
Site
Host
Site
Host
IPsec
Tunnels
Remote
Host
Remote
Host
FW/
VPN
  Encrypts entire IP packet
    Adds new header for next hop

## Slide 34: BGP security

## Slide 35: Recap: BGP security issues
An AS can claim to serve a prefix that they actually don’t have a route to
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
AS may forward packets along a route different from what is advertised
  Tell customers about fictitious short path…
  Much harder to fix!

## Slide 36: Security goals for BGP
Secure message exchange between neighbors
  Confidential BGP message exchange
  No denial of service
Validity of the routing information
  Origin authentication
  AS path authentication
  AS path policy
Correspondence of the forwarding path
  Does the traffic follow the advertised AS path?

## Slide 37: Prefix hijacking
Another OS originates the prefix
  BGP does not verify that the AS is authorized
  Registries of prefix ownership can be stale and inaccurate
Consequences for the affected ASs
  Blackhole: Data traffic is discarded
  Snooping: Data traffic is inspected; then redirected
  Impersonation: Data traffic is sent to bogus destinations
There can also be sub-prefix hijacking

## Slide 38: Hijacking is hard to detect
Legitimate origin AS doesn’t see the problem
  Picks its own route; may not even learn of the bogus
May not cause loss of connectivity
  E.g., if the bogus AS snoops and redirects
  May only cause performance degradation
Loss of connectivity may be isolated
  E.g., only for sources in parts of the Internet

## Slide 39: How to diagnose prefix hijacking?
Needs many vantage points across the Internet
  Analyze updates from many vantage points
  Launch traceroute from many vantage points
  Requires access to BGP routers or hosts across the Internet

## Slide 40: Feb 24, 2008 YouTube outage (100 minutes – 2 hours)
YouTube (AS 36561)
  Address block 208.65.152.0/22
Pakistan Telecom (AS 17557)
  Receives govt. order to block YouTube access
  Starts announcing 208.65.153.0/24 to its provider PCCW (AS 3491)
  All packets directed to YouTube get dropped
Mistakes were made
  AS 17557: Announced to everyone, not just customers
  AS 3491: Not filtering routes announced by AS 17557

## Slide 41: Many other issues
BGP session security
AS path validity
  Remove, add, or modify ASes in AS path
Forwarding issues
  Routing does not mean nor control forwarding
Overall, BGP today is
  Vulnerable
  Hard to fix (even though we have some solutions like S-BGP and BGPsec)

## Slide 42: Physical and link layer issues

## Slide 43: Eavesdropping/sniffing
For subnets using broadcast technologies (e.g., WiFi, pre-2000 Ethernet), it’s free
For any technology, routers/switches transferring the data can look at/capture/export data

## Slide 44: Denial of Service (DoS)
Overload/jam signals (e.g., in wireless networks)
Introduce ill-formed frames/packets
Just drop frames/packets

## Slide 45: Spoofing
Introduce forged frames/packets
More powerful when combined with eavesdropping
  We’ve seen its examples already in upper layers

## Slide 46: DHCP vulnerabilities
Attacker can listen to DHCP requests that new host broadcast
Can respond with forged offers before the actual DHCP server
  Essentially, taking over DNS, gateway, and other core information, and insert itself as a man-in-the-middle

## Slide 47: Summary
Ensuring network security is a constant battle
  AND, a vast field on its own
  We just looked at a few random samples
Next lecture: Final overview

## Slide 48: Thanks! Q&A