## Slide 1: EN.601.414/614 Computer Networks Wireless
Xin Jin
Fall 2020 (TuTh 1:30-2:45pm on Zoom)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
Wireless network basics
802.11 Wireless LAN

## Slide 3: Elements of a wireless network
network
infrastructure

## Slide 4: Elements of a wireless network
network
infrastructure
Wireless hosts
Laptop, smartphone
Run applications
May be stationary (non-mobile) or mobile
  Wireless does not always mean mobility

## Slide 5: Wireless vs. mobile
Wireless networks deal with communication over wireless links
Mobility deals with handling mobile users that change point of attachment to network
  Non-wireless networks may also have to deal with mobility issues
  Handoff: Mobile changes base station providing connection into wired network

## Slide 6: Elements of a wireless network
network
infrastructure
Base station
Typically connected to wired network
Relay: responsible for sending packets between wired network and wireless host(s) in its “area”
  E.g., cell towers, 802.11 access points (AP)

## Slide 7: Elements of a wireless network
network
infrastructure
Wireless link
Typically used to connect mobile(s) to base station
Also used as backbone link
Multiple access protocol coordinates link access
Various data rates, transmission distance

## Slide 8: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 9: Two modes of operation
Infrastructure mode: Base stations connect mobiles to wired network
Ad-hoc mode: Wireless hosts organize themselves to communicate

## Slide 10: Infrastructure mode
network
infrastructure

## Slide 11: Ad-hoc mode
No base station
Nodes can only transmit to other nodes within link coverage
Nodes organize themselves into a network: route among themselves

## Slide 12: Wireless network taxonomy
Single hop
Multiple hops
Infrastructure
(e.g., APs)
No
infrastructure
Host connects to
base station (WiFi,
WiMAX, cellular),
which connects to
larger Internet
No base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
Host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
No base station, no
connection to larger
Internet. May have to
relay to reach other
given wireless node
MANET, VANET

## Slide 13: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)

## Slide 14: Path loss/path attenuation
Free Space Path Loss (FSPL):
  d = distance
  λ = wave length (c/f)
  f = frequency
  c = speed of light
Due to
  Reflection, diffraction, absorption, terrain contours (urban, rural, vegetation), humidity
( )
FSPL =
4πdf
c
2
Notes: reduction in power density (attenuation) of an electromagnetic wave as it propagates through space.
Path loss may be due to many effects, such as free-space loss,refraction, diffraction, reflection, aperture-medium coupling loss, and absorption. Path loss is also influenced by terrain contours, environment (urban or rural, vegetation and foliage), propagation medium (dry or moist air), the distance between the transmitter and the receiver, and the height and location of antennas.

## Slide 15: SNR and BER
SNR: Signal-to-noise ratio
  Larger SNR makes it easier to extract signal from noise (good)
BER: Bit error rate
SNR vs. BER tradeoffs
  Given physical layer: Increase power → increase SNR → decrease BER
  Given SNR: Choose physical layer that meets BER requirement, giving highest throughput
  SNR may change with mobility: Dynamically adapt physical layer
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
Notes: BPSK: Binary phase-shift keying
QAM: Quadrature amplitude modulation

## Slide 16: Dealing with bit errors
Wired vs. wireless links: most loss due to congestion vs. higher, time-varying bit error rate (BER)
Dealing with high wireless bit error rates
  Sender could increase transmission power
    Needs high energy (bad for battery-powered hosts)
    Creates more interference with other senders
  Stronger error detection and recovery
    More powerful error detection/correction codes
    Link-layer retransmission of corrupted frames
  Many TCP alternatives/extensions for wireless
    TCP Westwood uses Explicit Loss Notification (ELN)

## Slide 17: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving at destination at slightly different times

## Slide 18: Multipath effects
Signals bounce off surface and interfere with one another
Self-interference
18
S
R
Ceiling
Floor

## Slide 19: Wireless link characteristics
Three important differences from wired link …
  Decreased signal strength: Radio signal attenuates as it propagates through matter (path loss)
  Multipath propagation: Radio signal reflects off objects ground, arriving ad destination at slightly different times
  Interference from other sources: Standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
… make communication across (even a point-to-point) wireless link much more “difficult”

## Slide 20: Wireless network characteristics
Broadcast medium
  Anybody in proximity can hear and interfere
Cannot receive while transmitting
  Our own (or nearby) transmission is deafening our receiver ⇒ Half-duplex
  Recent work has shown that full duplex may also be possible
Signals sent by sender don’t always end up at receiver intact
Notes: Broadcast – anybody in proximity can hear and interfere (assuming the same channel)
Half-duplex: Not an engineering problem – but a fundamental physics that our strong transmission is deafening to our receiver.
Solve by different channels/bands for RX/TX

## Slide 21: Wireless network characteristics
Multiple wireless senders and receivers create many problems
  Multiple access issues (we’ve seen this before)
  Hidden terminal problem

## Slide 22: Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
Hence, A, C are unaware of their interference at B
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 23: 802.11 wireless LAN (aka WiFi)
Many variations
  802.11b, 802.11a, 802.11g, 802.11n
All use CSMA/CA for multiple access
All have infrastructure and ad-hoc modes

## Slide 24: 802.11 LAN architecture
Wireless host communicates with base station
  Base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains
  Wireless hosts
  Access point (AP): base station
Ad-hoc mode: hosts only
BSS 1
BSS 2
Internet

## Slide 25: 802.11 LAN architecture
Designed for limited area
AP is set to specific channel
  Broadcast beacon messages with SSID (Service Set Identifier) and MAC Address periodically
Hosts scan all the channels to discover the AP’s
  Host associates with AP
BSS 1
BSS 2
Internet

## Slide 26: 802.11: Passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
Passive scanning
Beacon frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
Active scanning
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent from H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 27: 802.11 multiple access
802.11 CSMA: sense before transmitting
  Don’t collide with ongoing transmissions by others
802.11 has no collision detection!
  Difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  Can’t sense all collisions in any case: hidden terminal, fading
Avoid collisions: CSMA/CA
  CA: Collision Avoidance

## Slide 28: Basic collision avoidance
Carrier sense:
  When medium busy, choose random interval
  Wait that many idle timeslots to pass before sending
When a collision is inferred, retransmit with binary exponential backoff (like Ethernet)
  Use ACK from receiver to infer “no collision”
  Use exponential backoff to adapt contention window
Notes: Why do we wait?
Why not just send right away as medium becomes clear?

## Slide 29: CSMA/CA
Before every data transmission
  Sender sends a Request to Send (RTS) frame with the length of transmission and the destination
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK
If sender doesn’t get a CTS back, it assumes collision
Sender
Receiver
Other node in
sender’s range
RTS
ACK
Data
CTS
Notes: 29

## Slide 30: RTS/CTS
Works by reserving the channel using short frames before transferring much longer DATA frame
  Explicitly reserving the channel enables avoidance
Required to avoid hidden terminals
  Hidden terminals will hear CTS from the receiver

## Slide 31: Preventing collisions altogether
Frequency Spectrum partitioned into several channels
  Nodes within interference range can use separate channels
  Now A and C can send without any interference!
  Aggregate network throughput doubles
A
B
C
D

## Slide 32: 802.11 frame: Addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 33: Why do we need Address 3?
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame

## Slide 34: 802.11: Mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
Switch: which AP is associated with H1?
  Self-learning: Switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 35: 802.15: Personal area network
802.15: evolved from Bluetooth specification
Less than 10 m diameter
Replacement for cables (mouse, keyboard, headphones)
Ad-hoc: no infrastructure
Master/slaves:
  Slaves request permission to send (to master)
  Master grants requests
M
radius of
coverage
S
S
S
P
P
P
P
M
S
Master device
P
Slave device
Parked device (inactive)

## Slide 36: Summary
Wireless networking introduces more challenges than wired networks
  Interference, attenuation, multipath, hidden terminals, etc.
CSMA/CD doesn’t work because collision detection is difficult
  Instead, CSMA/CA is used that avoid collisions by reserving the channel a priori

## Slide 37: Thanks! Q&A