## Slide 1: EN.601.414/614 Computer Networks Inter-Domain Routing
Xin Jin
Spring 2019 (MW 3:00-4:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Final Exam
Time: 6pm-7:30pm, Wednesday, May 8
Location: Shaffer 301
Form: Closed-book
  Can bring TWO A4/letter papers with notes on both sides
  Can bring a calculator
  Anything else is prohibited
Focus on materials after midterm
  Materials before midterm will be tested, but not a focus

## Slide 3: Recap: Link-state routing
Every router knows its local “link state”
  Router u: “(u,v) with cost=2; (u,x) with cost=1”
Each router floods its local link state to all other routers in the network
  Does so periodically or when its link state changes
Every router learns the entire network graph
  Each runs Dijkstra’s Shortest-Path First (SPF) algorithm locally to compute forwarding table

## Slide 4: Recap: Distance-vector protocol
Link-state routing protocol
  Each node broadcasts its local information
Distance-vector routing protocol
  The opposite (sort of)
  Each node tells its neighbors about its global view

## Slide 5: Recap: Distance vector algorithm
From time-to-time, each node sends its own distance vector estimate to neighbors
When x receives new DV estimate from neighbor, it updates its own DV using B-F equation
  Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Eventually, the estimate Dx(y) may converge to the actual least cost dx(y)

## Slide 6: Recap: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 7: Agenda
Inter-domain routing

## Slide 8: Context and terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”
“Border Routers”

## Slide 9: AS-level Internet
Internet Inter-Domain Traffic, SIGCOMM, 2010

## Slide 10: Autonomous systems (AS)
An AS is a network under a single administrative control
  Currently over 55,000 ASes
  Updated daily at http://www.cidr-report.org/as2.0/
ASes are sometimes called “domains”
Each AS is assigned a unique identifier (ASN)

## Slide 11: “Intra-domain” routing: Within an AS
Link-State (e.g., OSPF) and Distance-Vector (e.g., RIP)
Primary focus
  Finding least-cost paths
  Fast convergence

## Slide 12: “Inter-domain” routing: Between ASes
Two key challenges
  Scaling
  Administrative structure
    Issues of autonomy, policy, privacy

## Slide 13: Recall: Addressing (so far)
Each host has a unique ID
No particular structure to those IDs

## Slide 14: Recall: Forwarding
111010010
MIT
#1
#2
#3
#4
Dst | Next Hop
JHU | 1
UCB | 3
MIT | 2
NYU | 4
#0
Forwarding Table @ #0
To JHU
To MIT
To UCB
To NYU
#6

## Slide 15: Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 16: Scaling
A router must be able to reach any destination
  Given packet’s destination address, lookup next hop
Naive: Have an entry for each destination
  There would be over 109 entries!
  AND routing updates per destination!
How can we improve scalability?
  We have already seen an example: longest-prefix matching

## Slide 17: A smaller table at node B?
Destination | Next Hop
to 1 | A
to 2 | C
to 3 | C
to 4 | A
to 5 | C
to 6 | A
to 7 | A
to 8 | C
1
7
4
6
A
B
C
2
5
8
3

## Slide 18: Re-number the end-systems?
Careful address assignment  can aggregate multiple addresses into one range  scalability!
Akin to reducing the number of destinations
Destination | Next Hop
to [1-4] | A
to [5-8] | C
1
3
4
2
A
B
C
6
5
8
7

## Slide 19: Scaling
A router must be able to reach any destination
Naive: Have an entry for each destination
Better: Have an entry for a range of addresses
  Can’t do this if addresses are assigned randomly!
  How addresses are allocated will matter!
Host addressing is key to scaling

## Slide 20: Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 21: Administrative structure shapes inter-domain routing
ASes want freedom in picking routes
  “My traffic can’t be carried over my competitor’s network”
  “I don’t want to carry A’s traffic through my network”
  Not expressible as Internet-wide “least cost”
ASes want autonomy
  Want to choose their own internal routing protocol
  Want to choose their own policy
ASes want privacy
  Choice of network topology, routing policies, etc.

## Slide 22: Choice of routing algorithm
Link-state
  No privacy – broadcasts all network information
  Limited autonomy – needs agreement on metric, algo
Distance-vector is a decent starting point
  Per-destination updates give some control
  BUT wasn’t designed to implement policy
  AND is vulnerable to loops
The “Border Gateway Protocol” (BGP) extends distance-vector ideas to accommodate policy

## Slide 23: Agenda
Inter-domain-routing
  Addressing (Scalability)
  BGP (Autonomy, policy, privacy)
    Context and basic ideas: today
    Details and issues: next lecture

## Slide 24: IP addressing

## Slide 25: Goal of addressing: Scalable routing
State: Small forwarding tables at routers
  Much less than the number of hosts
Churn: Limited rate of change in routing tables
Ability to aggregate addresses is crucial for both

## Slide 26: Aggregation works if…
Groups of destinations reached via the same path
These groups are assigned contiguous addresses
These groups are relatively stable
Few enough groups to make forwarding easy
1
3
4
2
A
B
C
6
5
8
7

## Slide 27: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 28: IP addresses (IPv4)
Unique 32-bit number associated with a host
Represented with the “dotted-decimal” notation
  e.g., 12.34.158.5
00001100
00100010
10011110
00000101
12
34
158
5
00001100
00100010
10011110
00000101

## Slide 29: Hierarchy in IP addressing
32 bits are partitioned into a prefix and suffix components
Prefix is the network component; suffix is the host component
Inter-domain routing operates on network prefix
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 30: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 31: CIDR example
Suppose a network has 50 computers
  Allocate 6 bits for host addresses (25 < 50 < 26)
  Remaining 32 - 6 = 26 bits as network prefix
Flexible boundary means the boundary must be explicitly specified with the network address!
  Informally, “slash 26”  128.23.9/26
  Formally, prefix represented with a 32-bit mask: 255.255.255.192, where all network prefix bits set to “1” and host suffix bits to “0”
  Also known as subnet mask (a group of machines with the same prefix are in the same subnet)

## Slide 32: Before CIDR: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 33: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 34: Allocation done hierarchically
Internet Corporation for Assigned Names and Numbers (ICANN) gives large blocks to…
Regional Internet Registries, such as the American Registry for Internet Names (ARIN), which give blocks to…
Large institutions (ISPs), which give addresses to…
Individuals and smaller institutions
FAKE Example:
  ICANN  ARIN  AT&T  JHU  CS

## Slide 35: CIDR: Addresses allocated in contiguous prefix chunks
Recursively break down chunks as get closer to host
12.0.0.0/8
12.0.0.0/15
12.253.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
12.3.0.0/22
12.3.4.0/24
:
:
12.3.254.0/23
12.253.0.0/19
12.253.32.0/19
12.253.64.0/19
12.253.64.108/30
12.253.96.0/18
12.253.128.0/17
:
:
:
:

## Slide 36: FAKE example in more detail
ICANN gave ARIN several /8s
ARIN gave AT&T one /8, 12.0/8
  Network Prefix: 00001100
AT&T gave JHU a /16, 12.34/16
  Network Prefix: 0000110000100010
JHU gave CS a /24, 12.34.56/24
  Network Prefix: 000011000010001000111000
CS gave me specific address 12.34.56.78
  Address: 00001100001000100011100001001110

## Slide 37: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 38: IP addressing  Scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy

## Slide 39: IP addressing  Scalable routing?
AT&T a.0.0.0/8
France Telecom
MIT a.b.0.0/16
JHU a.c.0.0/16
a.c.*.* is this way
a.b.*.* is this way

## Slide 40: IP addressing  Scalable routing?
AT&T a.0.0.0/8
France Telecom
MIT a.b.0.0/16
JHU a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16
Can add new hosts/networks without updating
the routing entries at France Telecom

## Slide 41: IP addressing  Scalable routing?
AT&T a.0.0.0/8
MIT a.b.0.0/16
JHU a.c.0.0/16
ESNet
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*

## Slide 42: IP addressing  Scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy
May not be able to aggregate addresses for “multi-homed” networks
  A multi-homed network is connected to more than one ASes for fault-tolerance, load balancing, etc.

## Slide 43: BGP: Border Gateway Protocol

## Slide 44: BGP (Today)
The role of policy
  What we mean by it
  Why we need it
Overall approach
  Four non-trivial changes to DV

## Slide 45: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 46: Topology & policy shaped by inter-AS business relationship
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic
Notes: Ehy???

## Slide 47: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 48: Why peer?
A
B
C
D
E
D and E communicate a lot
Peering saves B and C money

## Slide 49: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 50: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
An AS only carries traffic to/from its own customers over a peering link

## Slide 51: Routing follows the money!
A
B
E
Pr
Cu
Peer
Peer
Routes are “valley” free (more details later)

## Slide 52: In short
AS topology reflects business relationships between ASes
Business relationships between ASes impact which routes are acceptable

## Slide 53: BGP (Today)
The role of policy
  What we mean by it
  Why we need it
Overall approach
  Four non-trivial changes to DV

## Slide 54: Inter-domain routing: Setup
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Links represent both physical links and business relationships
BGP (Border Gateway Protocol) is the Inter-domain routing protocol
  Implemented by AS border routers

## Slide 55: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
You’ve heard this story before!
Notes: Arrows are routing message

## Slide 56: BGP inspired by Distance-Vector
Per-destination route advertisements
No global sharing of network topology information
Iterative and distributed convergence on paths
With four crucial differences!

## Slide 57: BGP & DV differences: (1) Not picking shortest-path routes
BGP selects the best route based on policy, not shortest distance (i.e., least-cost)
AS A may prefer “A,B,C” over “A,C”
How do we avoid loops?
A
B
C

## Slide 58: BGP & DV differences: (2) Path-Vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
C
B
A
d
“d: path (B,A)”
“d: path (A)”
data traffic
data traffic

## Slide 59: BGP & DV differences: (2) Path-Vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  Loop avoidance is straightforward (simply discard paths with loops)
  Flexible and expressive policies based on entire path

## Slide 60: BGP & DV differences: (3) Selective route advertisement
For policy reasons, an AS may choose not to advertise a route to a destination
Hence, reachability is not guaranteed even if graph is physically connected
A
B
C
AS-C does not want to carry traffic to AS-B

## Slide 61: BGP & DV differences: (4) BGP may aggregate routes
For scalability, BGP may aggregate routes for different prefixes
AT&T a.0.0.0/8
France Telecom
MIT a.b.0.0/16
JHU a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16

## Slide 62: Summary
Two key challenges in inter-domain routing
  Scaling (Addressing)
  Administrative structure (BGP)
    Issues of autonomy, policy, privacy
Next lecture: BGP policies, protocol, and challenges

## Slide 63: Thanks! Q&A