## Slide 1: EN.601.414/614 Computer Networks BGP
Xin Jin
Spring 2019 (MW 3:00-4:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
BGP policies and how they are implemented
BGP protocol details
BGP issues in practice

## Slide 3: Topology & policy shaped by inter-AS business relationship
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic
Notes: Ehy???

## Slide 4: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed

## Slide 5: Inter-domain routing: Setup
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Links represent both physical links and business relationships
BGP (Border Gateway Protocol) is the Inter-domain routing protocol
  Implemented by AS border routers

## Slide 6: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
Notes: Arrows are routing message

## Slide 7: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 8: BGP policies

## Slide 9: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 10: Typical selection policies
In decreasing order of priority
  Make/save money (send to customer > peer > provider)
  Maximize performance (smallest AS path length)
  Minimize use of my network bandwidth (“hot potato”)
  …

## Slide 11: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 12: Gao-Rexford
Peers
Providers
Customers
With Gao-Rexford, the AS policy graph is a DAG (directed acyclic graph) and routes are “valley free”

## Slide 13: Valley-Free Routing
Number links as (+1, 0, -1) for customer-to-provider, peer and provider-to-customer
In any path should only see sequence of +1, followed by at most one 0, followed by sequence of -1

## Slide 14: BGP Protocol details

## Slide 15: Who speaks BGP?
Border router
Border routers in an Autonomous System
Internal router

## Slide 16: What does “speak BGP” mean?
Implement the BGP protocol standard
  Read more here: http://tools.ietf.org/html/rfc4271
Specifies what messages to exchange with other BGP “speakers”
  Message types (e.g., route advertisements, updates)
  Message syntax
How to process these messages
  E.g., “when you receive a BGP update, do…. “
  Follows BGP state machine in the protocol spec + policy decisions, etc.

## Slide 17: BGP sessions: External
Border routers in an AS speaks BGP with border routers in other ASes using eBGP sessions

## Slide 18: BGP sessions: Internal
A border routers speaks BGP with other routers in the same AS using iBGP sessions

## Slide 19: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability
  E.g., OSPF, RIP

## Slide 20: eBGP, iBGP, and IGP together
Learn routes to external destination using eBGP
Distribute externally learned routes internally using iBGP
Travel shortest path to egress using IGP

## Slide 21: Basic messages in BGP
Open
  Establishes BGP session (BGP uses TCP)
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keep-alive
  Inform neighbor that connection is still viable

## Slide 22: Route updates
Format <IP prefix: route attributes>
  Attributes describe properties of the route
Two kinds of updates
  Announcements: new routes or changes to existing routes
  Withdrawal: remove routes that no longer exist

## Slide 23: Route attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  I.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss a few

## Slide 24: Attributes: (1) ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88
128.112.0.0/16
AS path = 7018 88
AS 7018
AT&T
AS 12654

## Slide 25: Attributes: (2) LOCAL PREF
Local preference in choosing between different AS paths
  Local to an AS; carried only in iBGP messages
The higher the value the more preferred
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:
Destination | AS Path | Local Pref
140.20.1.0/24 | AS3 AS1 | 300
140.20.1.0/24 | AS2 AS1 | 100
Notes: Because communicated to all IBGP routers within AS, all routers have a common view of how to exit the AS.
This differs from MED in 2 ways: (1) the destination prefix can be anywhere in the internet, not just in the next AS (as in the case for MED). (2) the AS that sets Local_Pref, is also the one that uses it. This allows one node to tell everyone locally what the best way out is.
MED can’t be used in this example because there is exactly one connection between any pair of AS’s.

## Slide 26: Attributes: (3) MED
Multi-exit discriminator is used when ASes are interconnected via 2 or more links; it specifies how close a prefix is to the link it is announced on
Lower is better
AS that announces a prefix sets MED
AS receiving the prefix (optionally!) uses MED to select link
Link B
Link A
MED=10
MED=50
AS1
AS2
AS3
destination prefix

## Slide 27: Attributes: (4) IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dest

## Slide 28: Using attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 29: BGP UPDATE processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets

## Slide 30: BGP issues in practice

## Slide 31: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies

## Slide 32: Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 33: Security
An AS can claim to serve a prefix that they do not have a route to (blackholing)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
AS may forward packets along a route different from what is advertised
  Tell customers about fictitious short path…
  Much harder to fix!
  More: http://queue.acm.org/detail.cfm?id=2668966

## Slide 34: Convergence
If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge
For arbitrary policies, BGP may fail to converge!

## Slide 35: Example of policy oscillation
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
“1” prefers “1 3 0”
over “1 0” to reach “0”
1
2
3
0

## Slide 36: Step-by-step of policy oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 37: Step-by-step of policy oscillation
1 advertises its path 1 0 to 2
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
advertise: 1 0

## Slide 38: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 39: Step-by-step of policy oscillation
3 advertises its path 3 0 to 1
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
advertise: 3 0

## Slide 40: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 41: Step-by-step of policy oscillation
1 withdraws its path 1 0 from 2
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
withdraw: 1 0

## Slide 42: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 43: Step-by-step of policy oscillation
2 advertises its path 2 0 to 3
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
advertise: 2 0

## Slide 44: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 45: Step-by-step of policy oscillation
3 withdraws its path 3 0 from 1
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
withdraw: 3 0

## Slide 46: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 47: Step-by-step of policy oscillation
1 advertises its path 1 0 to 2
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
advertise: 1 0

## Slide 48: Step-by-step of policy oscillation
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 49: Step-by-step of policy oscillation
2 withdraws its path 2 0 from 3
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
withdraw: 2 0

## Slide 50: We’re back to where we started
1
2
3
0
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0

## Slide 51: Convergence
If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge
For arbitrary policies, BGP may fail to converge!

## Slide 52: Performance nonissues
Internal routing
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy is not always about performance
  Policy-driven paths aren’t the shortest
AS path length can be misleading
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 53: AS path length can be misleading
An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that path 4 1 is better than path 3 2 1

## Slide 54: Real performance issue: Slow convergence
BGP outages are biggest source of Internet problems
Most popular paths are very stable
Outages are still very common
  Check out https://bgpstream.com/
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 55: BGP misconfigurations
BGP protocol is bloated yet underspecified
  Lots of attributes
  Lots of leeway in how to set and interpret attributes
  Necessary to allow autonomy, diverse policies
    But also gives operators plenty of rope
Configuration is mostly manual and ad hoc
  Disjoint per-router configuration to effect AS-wide policy
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 56: Summary
Network layer deals with data plane (forwarding) and control plane (routing)
Control plane deals with intra-domain routing (LS and DV) and inter-domain routing (BGP)
Next lecture: Layer 2

## Slide 57: Thanks! Q&A