## Slide 1: EN.601.414/614 Computer Networks Routing Algorithms
Xin Jin
Fall 2020 (TuTh 1:30-2:45pm on Zoom)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Agenda
Recap: least-cost path routing
Link-state routing
Distance-vector routing

## Slide 3: Recap: Least-cost path routing
Given: router graph & link costs
Goal: find least-cost path
  From each source router to each destination router
Easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop

## Slide 4: Recap: Dijkstra’s algorithm
Network topology, link costs known to all nodes
  All nodes have same info
Each node (“src”) computes least-cost paths to all other nodes
  After k iterations, know least-cost path to k destinations

## Slide 5: Recap: Dijkstra’s algorithm: Example
3
4
5
3
7
4
8
2
7
9
x
u
z
v
y
w
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
Notes:
Construct shortest path tree by tracing predecessor nodes
Ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 6: From routing algorithm to protocol
Dijkstra’s is a local computation!
  Computed by a node given complete network graph
Possibilities:
  Option#1: a separate machine runs the algorithm
  Option#2: every router runs the algorithm
The Internet currently uses Option#2

## Slide 7: Link-state routing
Every router knows its local “link state”
  Router u: “(u,v) with cost=2; (u,x) with cost=1”
Each router floods its local link state to all other routers in the network
  Does so periodically or when its link state changes
Every router learns the entire network graph
  Each runs Dijkstra’s Shortest-Path First (SPF) algorithm locally to compute forwarding table

## Slide 8: Flooding link state
Flooding
  A node sends its link-state info out all of its links
  The next node forwards the info on all of its links except the one the information arrived at
When to initiate flooding?
  Topology change (e.g., link/node failure/recovery)
  Configuration change (e.g., link cost change)
  Periodically
    To refresh link-state information (soft states)
    Typically (say) every 30 minutes

## Slide 9: Convergence
Why flood?
  To get all the nodes in the network to converge to the new topology
Upon convergence, all nodes will have consistent routing information and can compute consistent forwarding:
  All nodes have the same link-state database
  All nodes forward packets on shortest paths
  The next router on the path forwards to the expected next hop

## Slide 10: Convergence delay
Time to achieve convergence
Sources of convergence delay
  Time to detect failure
  Time to flood link-state information
  Time to re-compute forwarding tables
What happens if it takes too long to converge?

## Slide 11: Loop from convergence delay
3
4
5
3
7
4
8
2
7
9
x
u
z
v
y
w
u and w think that the path to y goes through v
3
4
5
3
7
4
8
2
7
9
x
u
z
v
y
w
v thinks that the path to y goes through w

## Slide 12: Performance during convergence period
Looping packets
Lost packets due to black holes
Out-of-order packets reaching the destination

## Slide 13: Link-state routing
Scalability?
  O(NE) messages
  O(N2) computation time
  O(Network diameter) convergence delay
  O(N) entries in forwarding table

## Slide 14: Link-state routing protocols
OSPF: Open Shortest Path First
IS-IS: Intermediate System to Intermediate System
  Similar to OSPF

## Slide 15: OSPF: Open Shortest-Path First
Open: publicly available
Uses link-state algorithm
  Link-state packet dissemination
  Topology map at each node
  Route computation using Dijkstra’s algorithm
Router floods OSPF link-state advertisements to all other routers in entire AS
  Carried in OSPF messages directly over IP (rather than TCP or UDP)
    Requires reliable transmission

## Slide 16: Distance-vector protocol
Link-state routing protocol
  Each node broadcasts its local information
Distance-vector routing protocol
  The opposite (sort of)
  Each node tells its neighbors about its global view

## Slide 17: Bellman-Ford equation
Let
  dx(y) := cost of least-cost path from x to y
Then
  dx(y) = minv {c(x, v) + dv(y) }
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 18: Bellman-Ford example
dx(z) = 9, dw(z) = 9, dv(z) = 6
du(z) = min {c(u,x) + dx(z),
c(u,w) + dw(z),
c(u,v) + dv(z) }
= min {5 + 9,
3 + 9,
7 + 6} = 12
Neighbor achieving the minimum (w) is next hop in shortest path, used in forwarding table
B-F equation says:
3
4
5
3
7
4
8
2
7
9
x
u
z
v
y
w

## Slide 19: Distance vector algorithm
Dx(y) is the estimate of least cost from x to y
  x maintains its own distance vector Dx = [Dx(y): y ∊ N]
Node x:
  Knows cost to each neighbor v: c(x,v)
  Maintains its neighbors’ distance vectors
    For each neighbor v, x has Dv = [Dv(y): y ∊ N]

## Slide 20: Distance vector algorithm
From time-to-time, each node sends its own distance vector estimate to neighbors
When x receives new DV estimate from neighbor, it updates its own DV using B-F equation
  Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Eventually, the estimate Dx(y) may converge to the actual least cost dx(y)

## Slide 21: Distance vector algorithm
Iterative, asynchronous
  Local iterations caused by
    Local link cost change
    DV update message from neighbor
Distributed
  Each node notifies neighbors only when its DV changes
    Neighbors then notify their neighbors if necessary
Wait for (change in local link cost OR msg from neighbor)
Recompute estimates
Notify neighbors if DV to any dest has changed
@each node:

## Slide 22: Example
x
z
y
7
2
1
2
0
1
x
y
y
z
z
3
1
0
x
y
y
z
z
3
1
0
2
0
1

## Slide 23: Example
0
1
x
z
y
7
1
x
y
y
z
z
3
1
0
4
routing loop!
x
y
y
z
z
3
1
0
2
0
1

## Slide 24: Example
x
y
y
z
z
3
1
0
4
0
1
x
z
y
7
1
routing loop!
0
1
x
y
y
z
z
3
1
0
4

## Slide 25: Example
x
y
y
z
z
5
1
0
4
0
1
x
z
y
7
1
routing loop!
0
1
x
y
y
z
z
3
1
0
4

## Slide 26: Example
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
4
0
1
4
routing loop!

## Slide 27: Example
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
4
0
1
6
routing loop!

## Slide 28: Example
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
5
1
0
6
0
1
6
routing loop!

## Slide 29: Example
0
1
x
z
y
7
1
x
y
y
z
z
5
1
0
x
y
y
z
z
7
1
0
6
0
1
6
routing loop!
Notes: .

## Slide 30: Example
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
6
0
1
6
routing loop!

## Slide 31: Example
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
6
0
1
8
routing loop!

## Slide 32: Example
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
8
0
1
8
routing loop!

## Slide 33: Example
0
1
x
z
y
7
1
x
y
y
z
z
7
1
0
x
y
y
z
z
7
1
0
8
0
1
8
routing loop!
Count-to-infinity scenario

## Slide 34: Problems with Bellman-Ford
Routing loops
  z routes through y, y routes through x
  y loses connectivity to x
  y decides to route through z
Can take a very long time to resolve
  Count-to-infinity scenario

## Slide 35: Poisoned reverse
One heuristic to avoid count-to-infinity
  If z routes to x through y,
    z advertises to y that its cost to x is infinite
  y never decides to route to x through z

## Slide 36
x
z
y
7
2
1
2
0
1
x
y
y
z
z
∞
1
0
x
y
y
z
z
3
1
0
2
0
1

## Slide 37
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
3
1
0
2
0
1
∞
∞

## Slide 38
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
3
1
0
0
1
∞
∞
∞

## Slide 39
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
∞
∞
∞

## Slide 40
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
∞
∞
7

## Slide 41
x
z
y
7
1
0
1
x
y
y
z
z
1
0
x
y
y
z
z
7
1
0
0
1
∞
7
8

## Slide 42: Poisoned reverse
One heuristic to avoid count-to-infinity
  If z routes to x through y,
    z advertises to y that its cost to x is infinite
  y never decides to route to x through z
Not guaranteed (why?)
Loop-free routing examples include
  Path vector
  Source tracing
Notes: Count-to-infinity can still happen if there are multiple nodes and the link-state messages are lost.

## Slide 43: Distance-vector routing
Scalability?
  Requires fewer messages than Link-State
  O(N) update time on arrival of a new DV from neighbor
  O(network diameter) convergence time
  O(N) entries in forwarding table
RIP is a protocol that implements DV (IETF RFC 2080)

## Slide 44: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (error propagates)

## Slide 45: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 46: Group Discussion
Topic: poisoned reverse
  Poisoned reverse is a heuristic to avoid count-to-infinity. How does it work? However, poisoned reverse cannot guarantee to avoid count-to-infinity. Can you give an example?
Discuss in groups, and each group chooses a leader to summarize the discussion
  Everyone should speak.
  Turn on your audio and video. Do not mute.

## Slide 47: Assignment 3
Intra-domain routing algorithms
  Design and implement simple versions of link state and distance vector protocols by yourself
  Hands-on experiences on routing protocols: real-world protocols in Cisco routers are just more complicated than the ones you designed and implemented!
  Use NetworkX to compute shortest path if you do not want to implement it yourself
Implement either link-state or distance-vector
  Implementing both gives you a bonus of 2 points

## Slide 48: Summary
Intra-AS routing
  Link-state routing
  Distance-vector routing
Next class: Midterm re-cap
Next Tuesday: Inter-AS routing

## Slide 49: Thanks! Q&A