## Slide 1: EN.601.414/614 Computer Networks CDN and DNS
Xin Jin
Spring 2019 (MW 3:00-4:15pm in Shaffer 301)
https://github.com/xinjin/course-net
Notes: Slides adapted from similar courses at Princeton, Stanford, UC Berkeley, University of Michigan, etc.

## Slide 2: Question on differences between connection and circuit
Connection
  A transport layer concept
  Resources are reserved at end hosts (sender & receiver)
  Need the underlying network layer to send data
Circuit
  A network layer concept
  Resources are reserved at each hop
  Circuit switching is one way to support a connection; packet switching is the other way

## Slide 3: Agenda
CDN: Content Distribution Network
DNS: Domain Name System

## Slide 4: Recap: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection

## Slide 5: Caching
Why does caching work?
  Exploit locality of reference
How well does caching work?
  Very well, up to a limit
  Large overlap in content
  But many unique requests
    Empirical result: effectiveness of caching (cache hit ratio) grows logarithmically with user size
Notes: Empirical result: under infinite cache capacity, Web cache hit ratio appears to grow logarithmically with the size of the user population served by the cache.

## Slide 6: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
If-modified-since: Wed, 18 Jan 2017 10:25:50 GMT
(blank line)

## Slide 7: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
Client specifies “if-modified-since” time in request
Server compares this against “last modified” time of resource
Server returns “Not Modified” if resource has not changed
…. or a “OK” with the latest version otherwise

## Slide 8: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
Response header:
  Expires – how long it’s safe to cache the resource
  No-cache – ignore all caches; always get resource directly from server

## Slide 9: Caching: Where?
Options
  Client (browser)
  Forward proxies
  Reverse proxies
  Content Distribution Network

## Slide 10: Caching: Where?
Many clients transfer same information
  Generate unnecessary server and network load
  Clients experience unnecessary latency
Server
Clients
Tier-1 ISP
ISP-1
ISP-2

## Slide 11: Caching with Reverse Proxies
Cache documents close to server
  Decrease server load
  By content provider
Clients
Tier-1 ISP
ISP-1
ISP-2
Reverse proxies

## Slide 12: Caching with Forward Proxies
Cache documents close to clients
  Reduce network traffic and decrease latency
  By ISPs or enterprises
Clients
Tier-1 ISP
ISP-1
ISP-2
Reverse proxies
Forward proxies

## Slide 13: Replication
Replicate popular Websites across many machines
  Spread load across servers
  Place content closer to clients
  Help when content isn’t cacheable

## Slide 14: Recap: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 15: Content Distribution Networks (CDN)
Caching and replication as a service
Large-scale distributed storage infrastructure (usually) administered by one entity
  e.g., Akamai has servers in 20,000+ locations
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)
Can do some processing to handle dynamic webpage content
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 16: Cost-effective content delivery
General theme: multiple sites hosted on shared physical infrastructure
  Efficiency of statistical multiplexing
  Economies of scale (volume pricing, etc.)
  Amortization of human operator costs
Examples:
  CDNs
  Web hosting companies
  Cloud infrastructure

## Slide 17: CDN example – Akamai
Akamai creates new domain names for each client
  e.g., a128.g.akamai.net for cnn.com
The client content provider modifies content so that embedded URLs reference new domains
  “Akamaize” content
  e.g., http://www.cnn.com/image-of-the-day.gif becomes http://a128.g.akamai.net/image-of-the-day.gif
Requests now sent to CDN’s infrastructure

## Slide 18: How to direct clients to particular replicas?
In order to
  Balancing load across server replicas
  Pairing clients with nearby servers to decrease latency and overall bandwidth usage

## Slide 19: DNS: Domain name system

## Slide 20: Internet names & addresses
Machine addresses: e.g., 141.212.113.143
  Router-usable labels for machines
  Conforms to network structure (the “where”)
Machine names: e.g., cs.jhu.edu
  Human-usable labels for machines
  Conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other
  A directory service

## Slide 21: Why?
Convenience
  Easier to remember www.google.com than 216.58.216.100
Provides a level of indirection!
  Decoupled names from addresses
  Many uses beyond just naming a specific host

## Slide 22: DNS: History
Initially all host-address mappings were in a hosts.txt file (in /etc/hosts):
  Maintained by the Stanford Research Institute (SRI)
  Changes were submitted to SRI by email
  New versions of hosts.txt periodically FTP’d from SRI

## Slide 23: DNS: History (cont’d)
As the Internet grew this system broke down
  SRI couldn’t handle the load
  Names were not unique
  Hosts had inaccurate copies of hosts.txt
The Domain Name System (DNS) was invented to fix this

## Slide 24: Goals
Uniqueness: no naming conflicts
Scalable
  Many names and frequent updates
Distributed, autonomous administration
  Ability to update my own (machines’) names
  Don’t have to track everybody’s updates
Highly available
Lookups are fast
Perfect consistency is a non-goal

## Slide 25: How?
Partition the namespace
Distribute administration of each partition
  Autonomy to update my own (machines’) names
  Don’t have to track everybody’s updates
Distribute name resolution for each partition
How should we partition things?

## Slide 26: Key idea: Hierarchy
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 27: Hierarchical namespace
“Top Level Domains” are at the top
Domains are subtrees
  e.g., .edu, jhu.edu, cs.jhu.edu
Name is leaf-to-root path
  cs.jhu.edu
Depth of tree is arbitrary (limit 128)
Name collisions trivially avoided
  Each domain is responsible
root
edu
com
gov
mil
org
net
uk
fr
jhu
princeton
cs
…

## Slide 28: Hierarchical administration
root
gov
mil
org
net
uk
fr
…
A zone corresponds to an administrative authority that is responsible for that portion of the hierarchy
  e.g., JHU controls names: *.jhu.edu
  e.g., CS controls names: *.cs.jhu.edu
ICANN/IANA
edu
com
jhu
princeton
cs
Notes: ICANN: Internet Corporation for Assigned Names and Numbers
IANA: Internet Assigned Numbers Authority

## Slide 29: Server hierarchy
Top of hierarchy: Root servers
  Location hardwired into other servers
Next Level: Top-level domain (TLD) servers
  .com, .edu, etc.
  Managed professionally
Bottom Level: Authoritative DNS servers
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority

## Slide 30: Server hierarchy
Each server stores a (small!) subset of the total DNS database
An authoritative DNS server stores “resource records” for all DNS names in the domain that it has authority for
Each server needs to know other servers that are responsible for the other portions of the hierarchy
  Every server knows the root
  Root server knows about all top-level domains

## Slide 31: DNS root
Located in Virginia, USA
How do we make the root scale?
Verisign, Dulles, VA

## Slide 32: DNS root servers
13 root servers (labeled A-M; see http://www.root-servers.org/)
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium
Palo Alto, CA
I Autonomica, Stockholm
K RIPE London
M WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign

## Slide 33: DNS root servers
13 root servers replicated via anycast
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium,
Palo Alto, CA
(and 37 other locations)
I Autonomica, Stockholm (plus 29 other locations)
K RIPE London (plus 16 other locations)
M WIDE Tokyo
plus Seoul, Paris, San Francisco
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles, NY, Chicago)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign (21 locations)
Notes: Each root server has one IP address and is replicated on many machines.

## Slide 34: Anycast in a nutshell
Routing finds shortest paths to destination
If several locations are given the same address, then the network will deliver the packet to the closest location with that address
Characteristics
  Very robust
  Requires no modification to routing algorithms

## Slide 35: DNS records
DNS servers store resource records (RRs)
  RR is (name, value, type, TTL)
Type = A: ( Address)
  name = hostname
  value = IP address
Type = NS: ( Name Server)
  name = domain
  value = name of DNS server for domain

## Slide 36: DNS records (cont’d)
Type = CNAME: ( Canonical Name)
  name = alias name for some “canonical” (real) name
    e.g., documents.example.com is really docs.example.com
  value = canonical name
Type = MX: ( Mail eXchanger)
  name = domain in email address
  value = name(s) of mail server(s)

## Slide 37: Inserting Resource Records into DNS
Register foobar.com at registrar (GoDaddy)
  Provide registrar with names and IP addresses of your authoritative name server(s)
  Registrar inserts RR pairs into the .com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.44.9.129, A)
Store resource records in your server dns1.foobar.com
  e.g., type A record for www.foobar.com
  e.g., type MX record for foobar.com

## Slide 38: Using DNS (Client/App View)
Two components
  Local DNS servers
  Resolver software on hosts
Local DNS server (“default name server”)
  Clients configured with default server’s address OR learn it via a host configuration protocol (e.g., DHCP)
Client application
  Obtain DNS name (e.g., from URL)
  Do gethostbyname() to trigger DNS request to its local DNS server
Notes: DHCP: Dynamic Host Configuration Protocol

## Slide 39: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
princeton.edu servers

## Slide 40: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
princeton.edu servers
www.princeton.edu?
(mydns.jhu.edu)

## Slide 41: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
www.princeton.edu?
princeton.edu servers
(mydns.jhu.edu)

## Slide 42: Name resolution
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
(mydns.jhu.edu)
www.princeton.edu?
princeton.edu servers

## Slide 43: Name resolution: Recursive
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
(mydns.jhu.edu)
www.princeton.edu?
princeton.edu servers

## Slide 44: Name resolution: Iterative
DNS client (me.cs.jhu.edu)
DNS server
root servers
local
.edu servers
www.princeton.edu?
princeton.edu servers

## Slide 45: Two ways to resolve a name
Recursive name resolution
  Ask server to do it for you
Iterative name resolution
  Ask server who to ask next
The iterative example we saw is a mix of both!

## Slide 46: DNS protocol
Query and Reply messages; both with the same message format
  Header: identifier, flags, etc.
  Plus resource records
  See text for details
Client–server interaction on UDP Port 53
  Spec supports TCP too, but not always implemented

## Slide 47: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available?

## Slide 48: Reliability
Replicated DNS servers (primary/secondary)
  Name service available if at least one replica is up
  Queries can be load-balanced between replicas
Usually, UDP used for queries
  Reliability, if needed, must be implemented on UDP
Try alternate servers on timeout
  Exponential backoff when retrying same server
Same identifier for all queries
  Don’t care which server responds

## Slide 49: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available
Fast lookups?

## Slide 50: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.cnn.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 51: Negative caching
Remember things that don’t work
  Misspellings like www.cnn.comm and www.cnnn.com
  These can take a long time to fail the first time
  Good to remember that they don’t work so the failure takes less time the next time around
Negative caching is optional
  Not widely implemented

## Slide 52: Important properties of DNS
Administrative delegation and hierarchy enables:
  Easy unique naming
  “Fate sharing” for network failures
  Reasonable trust model
  Caching increases scalability and performance

## Slide 53: DNS provides indirection
Addresses can change underneath
  Move www.cnn.com to 4.125.91.21
Name could map to multiple IP addresses
  Load-balancing (CDN)
  Reducing latency by picking nearby servers (CDN)
Multiple names for the same address
  E.g., many services (mail, www) on same machine
  E.g., aliases like www.cnn.com and cnn.com
This flexibility applies only within domain!

## Slide 54: Summary
CDNs improve web performance
  Via replication and caching
  Good server selection
DNS allows us to go to webpages without having to memorize IP addresses
  Allows a level of indirection that enables many functionalities including CDN server selection
Exercise and lab session this Wednesday
Assignment 1 is due this Friday

## Slide 55: Thanks! Q&A